## Slide 1: NEURON Tutorial
Nikki Pelot
Duke University – BME 515
Fall 2014
Notes: Note the hyperlinks throughout the slides.
Many of these concepts apply to computational neuroengineering outside of NEURON as well.

## Slide 2: What is NEURON?
“NEURON provides a powerful and flexible environment for implementing biologically realistic models of electrical and chemical signaling in neurons and networks of neurons.”
– Hines and Carnevale 2002
Notes: Originally developed at Duke! Now run out of Yale.

## Slide 3: Installing
Download and install latest release.
Mac
  Extra instructions
  Need latest developer tools
  Troubleshooting
Windows
  I use 32 bit Cygwin (even though I have a 64 bit machine).
  Troubleshooting
UNIX
Installation tips for each OS on the forum.
Avoid file paths with spaces.

## Slide 4: Resources
New programmer’s reference
  Use “Index” rather than “Quick search”
  Sometimes still useful to look at old version
  Useful to check if a given word is a built-in variable/keyword/etc.
ModelDB
  Often helpful to modify from existing code.
  MyFirstNEURON
Forum
Suggestions for how to develop models
Tutorials
  http://neuron.duke.edu/
  http://www.anc.ed.ac.uk/school/neuron/
  http://web.mit.edu/neuron_v7.3/nrntuthtml/tutorial/tutA.html
Notes: Can be useful to revisit the tutorials as you learn more.

## Slide 5
Ref.: http://www.neuron.yale.edu/neuron/static/docs/units/unitchart.html
Check your units when performing calculations in NEURON!

## Slide 6: Using NEURON: Two Camps
GUI
Coding
  NEURON file extensions
    .hoc (Higher Order Computing) or .py (Python)
      Scripts, like .m in Matlab
      Python implementation is much newer. I do not have
    .mod (NMODL)
      Membrane mechanisms
  No native text editor.
    Notepad, Notepad++, Geany, etc.
    Set language to C for most syntax highlighting or add NEURON-specific syntax highlighting.
Not mutually exclusive, can use one to design geometry, and the other to run simulations, for example.
Notes: I am biased towards coding.
Not mutually exclusive. For ex, you can design your neuron in hoc (code), then run your simulations using the GUI.

## Slide 7: GUI
Cell Builder tutorial
  What’s a session (.ses) file?
  Create a simple model axon with soma, dendrites, and axon. Specify geometry and biophysics.
Tutorial for the other main components
  Stimulating with current point source
  Running simulation
  Plotting results
  Saving session

## Slide 8: Inside NEURON
Cable model
Sections = Components of a neuron (soma, axon, dendrite, etc.)
Generated with “create” command
Recall equations for membrane resistance & capacitance, and axial resistances. See “Parameters of Cable Equation” on Sakai.
Every section is modeled as a cylinder and has the same parameters:
  Ra = Axial resistivity [Ω-cm]
  cm = Membrane specific capacitance [uF/cm2]
  L = Length [um]
  diam = Diameter [um]
  nseg = Number of segments
NOTE: Section ≠ Segment
Ref.: Wikipedia

## Slide 9: Note on Ra
An axon with perfectly insulating myelin is constructed by connecting nodes of Ranvier (NoR) with resistors modeling the intracellular space. However, these resistors should not merely account for the length of the NoR, but rather the length of the NoR + the length of the myelin.
Axial intracellular resistance: R = 4(Ra)(length)/π(diam)2
  Ra = intracellular resistivity
NEURON will compute R = 4(Ra)(L)/π(diam)2
You want R = 4(Ra)(L+INL)/π(diam)2
  INL = internodal length
Therefore, need to multiply Ra by (L+INL)/L
NoR
myelinated section
NoR
INL
L

## Slide 10: Working with Sections
Referring to section or its parts
section.parameter
section parameter
section { ...
}
access: subsequent commands without section reference will refer to this section

## Slide 11: Normalized Length & Sections vs Segments
Generate a section with “create” command.
NEURON uses normalized length, such that each section spans from 0 to 1.
Different sections have different parameters and/or properties. Separate sections must joined using the “connect” command.
connect soma(1), axon(0)
You can connect one segment at any point along another segment.
soma
axon
0
1
0
1
Notes: For example, the soma may only have passive membrane properties while the axon has HH channels. Or different diameters for different segments. However, note that it is possible to implement spatially varying parameters.

## Slide 12: Normalized Length & Sections vs Segments
Each section is divided into nseg segments (spatial discretization). You can access variables (such as Vm) at the center of each segment.
Ex.: For a section with one segment, you can access Vm halfway along the section:
myaxon.v(0.5)
But how many segments (nseg) do you need per section? In other words, how much spatial resolution is needed?
  Alternatively, you can have many small sections, each with nseg=1.
Notes: Spatial discretization

## Slide 13: Spatial & Temporal Resolutions
Best solution: Keep increasing resolution (smaller delta’s) until your results no longer change.
Practical solutions:
  Spatial resolution: d_lambda rule
    w/ f=100Hz
    Note: f=100Hz assumes ωRmCm >> 1 at 100Hz
    Set nseg (number of segments into which the section is divided) appropriately: Δx ≤ section length/# segments = L/nseg
  Temporal resolution
    Use fraction of time constant: τ=RmCm, but what’s Rm…?
    Typically use Δt≈0.001 to 0.005ms.

## Slide 14: “insert” command
Add extra layers to the cable to permit extracellular stimulation
  insert extracellular
    Reinitialize all e_extracellular(…) to zero for all segments of all sections, particularly if batching multiple simulations.
    More on extracellular stimulation later.
Add membrane mechanisms
  insert pas
    Passive mechanism
    Set g_pas and e_pas
  insert hh
    Hodgkin-Huxley
  insert axnode (from MRG model)
Additional mechanisms
  insert <.mod SUFFIX>
  Need to compile…

## Slide 15: NMODL: .mod files
NMODL = NEURON Model Description Language
Code for membrane mechanisms
Must be compiled with “mknrndll”:
  No spaces in file path.
  Same drive where NEURON is installed.
  Recompile when changing computers.

## Slide 16: Recording .mod State Variables
Identify state variable of interest in .mod file of a mechanism that was “inserted” into a section.
  Ex.: m, n, h
Identify SUFFIX in .mod file (same as used for “insert” statement).
Let’s say I have a section called “node” with nseg=1 and HH mechanism (SUFFIX = hh). I could access the gating variable halfway along my node:
node.m_hh(0.5)

## Slide 17: Classes
Any variable that isn’t a section or a number is part of a class
  Vector
  File
  IClamp
  APCount
  NetCon
  etc.
Declaring objects
objref object_name
object_name = new Class()
Note: objectvar = objref
  Compare: use create to declare sections; use objref or objectvar to declare a class object
Each class has its own associated functions and parameters
object_name.ClassFunction(…)
Notes: Keywords: objref or objectvar; new

## Slide 18: File Class Example
objref myfile
myfile = new File()
strdef file_name
sprint(file_name,”Data/MyResults%d.dat”,3)
myfile.wopen(file_name)
// or just myfile.wopen(“Data/MyResults3.dat”)
myfile.printf(“Header1 Header2 \n”)
myfile.printf(“%d %d”, result1, result2)
// Can print results within a for loop.
myfile.close()

## Slide 19: Vector Class Example
objref myvec
myvec = new Vector(num_elem, 0)
myvec.x[0] = 10
objref Vm_vec
Vm_vec = new Vector()
Vm_vec.record(&axon.v(0.2),dt)
Run simulation…
create node[num_nodes]
…
objref Vm_vec[num_nodes]
for K = 0, num_nodes-1 {
Vm_vec[K] = new Vector()
Vm_vec[K].record(&node[K].v(0.5),dt)
}
Other vector class functions: copy, min, max, printf, size, etc.

## Slide 20: File Class and Vector Class Example
objref Ve_data, Ve_file
Ve_file = new File()
Ve_file.ropen(fname)
Ve_data = new Vector(num_nodes, 0)
Ve_data = scanf(Ve_file)
Ve_data = Ve_data.mul(1000) // convert from V to mV
Ve_file.close()

## Slide 21: APCount Class Example
Use to detect action potentials
Note: Can also use NetCon to record spike times.
objref apc
myaxon apc = new APCount(0.1)
apc.thresh = -20
Detect an action potential when Vm at 0.1 along myaxon crosses -20mV with rising phase
if (apc.n >= 1) {
print “Detected ”, apc.n, “action potentials!”
} else {
print “No action potentials.”
}

## Slide 22: Code Structure
Modular coding.
Model specification
Model initialization
Instrumentation
  Stimulation
  Recording
Simulation control
Data post-processing & output
Notes: Modular coding. Want to design code such that it’s reusable.

## Slide 23: Code Structure
Usually, you should begin with
load_file("nrngui.hoc")
load_proc("nrnmainmenu")
Comments: “//”
No semi-colons!
Standard conditional statements…
  if ( … ) else if { … } else { … }
  for
  while
Subroutines:
  Procedures
  proc proc_name { … }
  proc_name()
  Functions
  func func_name { … return <double precision value> }
  func_name()
  Subroutines (proc or func) with input variables
  proc proc_name {
  myval = $1 * $2
  }
  proc_name(3.5, 6.243)

## Slide 24: Intracellular Stimulation
Intracellular: IClamp
objref stim
myaxon {
stim = new IClamp()
stim.loc(0.2)
stim.del = 5 // start time of stimulus [ms]
stim.amp = 4 // amplitude [nA]
stim.dur = 0.1 // duration of stimulus [ms]
}
~
0
1
0.2
myaxon
stim

## Slide 25: Extracellular Stimulation
Extracellular: IClamp + insert extracellular
  Need to…:
    “insert extracellular” for each section
    create a dummy section to which you can attach your IClamp
    manually apply extracellular potentials to each section (check units!!!)
Ref.: http://www.neuron.yale.edu/neuron/static/new_doc/modelspec/programmatic/mechanisms/mech.html#index-5

## Slide 26: Extracellular Stimulation
create nodes[num_nodes] // Could instead have one section with many segments
forall {
insert extracellular
}
...
objref stim
create myelec
myelec {
stim = new IClamp()
stim.loc(0.5)
stim.del = 5 // start time of stimulus [ms]
stim.amp = 4 // amplitude [nA]
stim.dur = 0.1 // duration of stimulus [ms]
}
...
while (t<tstop) {
for K = 0, num_nodes-1 {
// r_axon is a vector with the distance from the electrode to each node
nodes[K].e_extracellular = rhoe*stim.i/(4*pi*r_axon.x[K]) // check units!! [mV]
}
fadvance()
}
~
0
1
nodes
stim
myelec

## Slide 27: Running Simulation in hoc
finitialize(-85) // initialize to Vrest
white (t<tstop) {
fadvance()
}

## Slide 28: Saving & Analyzing Results
Save ASCII file: see File Class Example
Save binary file
  Binary file is smaller than text/ASCII file
  But then can’t just open in Notepad to see contents
  How? myvector.vwrite()
Analyzing data in Matlab
  >> importdata
  >> textscan
  etc.

## Slide 29: Saving & Analyzing Results
Plotting in hoc
objref g1
g1 = new Graph()
g1.size(…) // specify (xmin, xmax, ymin, ymax)
myvec.plot(g1)

## Slide 30: Other Notes
Declare sections (create), objects (objref, objectvar), and strings (strdef) outside of procedures and functions.
Indexing starts at 0 like C, not 1 like Matlab.
Recompile .mod files with mknrndll for specific machine.
.mod files must be in same directory as .hoc script.
Closing squiggly bracket “}” must be on its own line to end a loop/procedure/function.
Common error: your neuron has been overstimulated; lower amplitude…
exp(<big #>) out of range, returning exp(700)

## Slide 31: More Advanced Things…
Networks of neurons
  NetCon (“network connection”) class
Realistic morphologies
  ModelDB
  Neurolucida

## Slide 32: Coding example…