## Slide 1: BME 515 – Neural prosthetic systems
Brian Huynh, Jessie Wilson (Fall 2014)

## Slide 2: neuroSigma

## Slide 3
Trigeminal Nerve Stimulation
Non-invasive external TNS (eTNS) or minimally-invasive subcutaneous TNS (sTNS)
Treatment for epilepsy, depression, ADHD, and PTSD
Monarch™ eTNS system is approved in the EU (CE Mark approved in Sep 2012) and Canada for treatment of epilepsy and depression
In US, both eTNS™ and sTNS™ are limited to investigational use
Drug-resistant epilepsy (DRE) affects 30% of all people with epilepsy
2009: acute and long-term pilot feasibility study of eTNS for epilepsy
2013: randomized, double-blind, active control study of eTNS for safety and efficacy
Planned: Phase III randomized controlled trial
Monarch™ eTNS™ System
CE Mark approval for the adjunctive treatment of epilepsy and major depressive disorder
  For adults and children > 9 years old in EU
Sold by prescription in Canada to patients under physician supervision (Class 2 medical device license)
  For treatment of drug-resistant epilepsy (DRE), major depressive disorder (MDD), and treatment-resistant depression
Small stimulator (in pocket or waist) and electric patch on forehead
Patch stimulates trigeminal nerve through the surface of the skin, primarily used while patient is asleep
The eTNS System
Notes: http://www.neurosigma.com/tns.html
http://www.prnewswire.com/news-releases/neurosigma-receives-health-canada-approval-for-its-monarch-etns-system-for-the-treatment-of-drug-resistant-epilepsy-and-major-depressive-disorder-205733901.html

## Slide 4
Trigeminal Nerve Stimulation for Epilepsy: Long-Term Feasibility and Efficacy (DeGiorgio CM et al., 2009)
Why Trigeminal Nerve?
Three afferent branches that project to trigeminal ganglion and nucleus, which projects to nucleus tractus solitarious (NTS) and locus ceruleus, all of which play a role in inhibition of seizures
Antiepileptic effect of trigeminal nerve and related structures confirmed in animal models
Pentylenetetrazole model, HF stimulation of trigeminal nerve significantly reduced seizure severity and frequency
Bilateral more effective than unilateral stimulation
HF stimulation more effective than LF stimulation
Timeline
4-week pretreatment baseline
Evaluated at 1, 2, 3, 6, and 12 months
Methods
Patient (Inclusion) Criteria
18-65 years
≥3 complex-partial/generalized tonic-clonic seizures/month
Exposure to ≥2 antiepileptic drugs (AEDs)
Stimulation Parameters
frequency 120 Hz, 250 us, ≤30 seconds on, ≤30 seconds off for 12–24 hours/day, and 1.25-inch disposable, silver-gel, adhesive electrodes were utilized, spaced 2 inches apart
Stimulated ophthalmic nerve (V1) in all subjects, allowing for bilateral stimulation
Results
n=7 completed 12-month study
TNS well tolerated (side effects: skin irritation (n=5), tingling, forehead pressure, headache)
    No detectable effect on pulse, BP, or ECG
Mean reduction in seizure frequency of 59% at 12 months
Notes: http://www.neurology.org/content/72/10/936

## Slide 5
Randomized controlled trial of trigeminal nerve stimulation for drug-resistant epilepsy (DeGiorgio et al., 2013)
Information is current as of January 30, 2013
Study designed to provide Class II evidence for eTNS in drug-resistant partial seizures
Primary Outcomes: seizure frequency, responder rate, and time to the fourth seizure
Methods
Double-blind, randomized, active-control trial in DRE (drug-resistant epilepsy)
42 subjects w/ ≥ 2 partial onset seizures/month completed study
6-week baseline period (to calculate baseline seizure frequency) & evaluated at 6, 12, and 18 weeks during acute treatment period
Randomized to treatment (eTNS 120Hz) or control (eTNS 2Hz)
  Pulse duration < 250 us
  Active Control: Duty cycle: 2s ON, 90s OFF, pulse duration = 50 us
Targeted R and L branches of ophthalmic and supratrochlear nerves for bilateral stimulation
Results
On average, subjects failed 3.35 anti-epileptic drugs (AEDs) prior to enrollment
eTNS was well tolerated (side effects: anxiety (4%), headache (4%), skin irritation (14%))
Seizure Frequency (mean response ratio):
  Treatment Group: -13.9 ± 6.7
  Active Control Group: -9.0 ± 6.8
Responder Rate: >50% reduction in seizure frequency
  Treatment Group: 30.2%
  Active Control Group: 21.1%
Time to 4th Seizure: Not significant
  Treatment: net decrease 2.5 days or 20%
  Control: net decrease 5 days or 21.7%
Discussion
Expected n > 200 and higher seizure frequency (≥ 4 seizures/month) for inclusion for phase III multicenter study
Change active control parameters to reduce possibility of placebo response
Notes: http://www.neurology.org/content/80/9/786.full.html

## Slide 6
Notes: Neurology-2003-DeGiorgio-421-2: http://www.neurology.org/content/61/3/421.long