## Slide 1: Neuromodulation techniques in the treatment of the overactive bladder
J. Groen and J.L.H.R. Bosch
Department of Urology, Erasmus Medical Center Rotterdam, Rotterdam, The Netherlands

## Slide 2
Mechanism of Action
Spinal Inhibitory Mechanisms of the Micturition Reflex:
Guarding reflex
  Increased activity of striated urethral sphincter in response to bladder filling
  Reflexively induces detrusor (bladder wall muscle) relaxation
  Edvarsen’s reflex
    Increased activity of the sympathetic nervous system in response to bladder filling
  Anal dilation
    Afferent pathway
    Anorectal branches of the pelvic nerve
    Prevents voiding during defecation
    Gentle mechanical stimulation of the genital region
    Afferent pathway
    Dorsal clitoral or penile branches of pudendal nerve
    Prevents voiding during intercourse
    Physical activity
    Afferent pathway
    Muscle afferents from limbs (but not pelvic floor)
    Prevents voiding during fighting or fleeing
Introduction
Current neuromodulation techniques for treating overactive bladder
Anogenital electrical stimulation
Transcutaneous electrical nerve stimulation (TENS)
Sacral nerve neuromodulation
Percutaneous posterior tibial nerve stimulation (Stoller afferent nerve stimulation, SANS)
Magnetic stimulation
Potential Mechanisms
Activation of efferent fibers to the striated urethral sphincter reflexively cause detrusor relaxation
Activation of afferent fibers causes inhibition at a spinal or a supraspinal level
Electrical Parameters
Bipolar square-wave pulses
Pulse duration: 0.2-0.5 ms is optimal, but 1 ms also used
Stimulation frequency: optimal is 5-10Hz
  <10 Hz uncomfortable at higher amplitudes
Desired pulse amplitude should be as high as possible for anogenital stimulation
Desired pulse amplitude should be just above detection threshold for sacral nerve modulation

## Slide 3: ANOGENITAL STIMULATION
Anogenital Stimulation
Technique
Long-term or chronic stimulation: for stress incontinence and not discussed here
Short-term or acute stimulation
Limited sessions
Intensity as high as possible (i.e. just below discomfort level)
Overactive bladder and mixed incontinence
Evidence
Published results vary considerably
Beneficial effect in about half of the patients
Treatment compared with sham
Most authors found active treatment was symptomatically and cystometrically superior to sham
Suitable Patients
Success rates depend heavily on selection of patients
Failure of pharmacological treatment does not exclude good response
Treatment Scheme and Parameters
Intensity should be as high as possible
Long-term Effectiveness
Few studies reported success rates after a follow-up of >6 months
Yamanishi et al: 2 year follow up, 64% subjective satisfaction
Eriksen et al: 85% initially to 77% after 1 year
Bratt et al: 60% satisfied after 10 years
Side Effects
No severe side effects
Local pain and diarrhea disappear after brief pause in therapy
Mucosal irritation seldom occurs

## Slide 4: Transcutaneous electrical nerve stimulation (TENS)
TENS
Technique
Electrodes over S2 and S3 dermatomes
Daily stimulation for a few weeks
Stimulation intensity should not exceed discomfort level
Evidence
Acute cystometric effects shown in patients w/ unstable bladder
Walsh et al: 76% and 60% improvement in daytime frequency and urgency, respectively
56% reduction of nocturia
Site of Stimulation
Various reported sites
Conflicting published results
Long-term Results
Not useful unless clinical or home re-treatment
Therapeutic effects outlast treatment period only by a few months
Side Effects
No major complications
Local skin irritation

## Slide 5: Sacral Nerve Neuromodulation
Sacral Nerve Neuromodulation
Sacral nerve stimulation, SNS, InterStim therapy
Continuous stimulation and close nerve contact
IPG w/ electrode stimulating sacral nerve S3
Implantation only if successful peripheral nerve evaluation (PNE) test
Technique
Patients w/ incontinence more than halved during PNE test may receive permanent implant
Foramen electrode fixed to sacrum, extension cable, and subcutaneous pulse generator
Evidence
Bosch: 60-70% patients responded to test stimulation
Correlation b/t urodynamic and symptomatic improvements is only partial
Suitable Patients
PNE test
Men do less well than women
Psychological factors are important
Neurogenic cause of bladder overactivity is not reason for exclusion
Long-term Effectiveness
Cure rate decreased from 80% and 65% after 1 and 1.5 years, respectively, but remained constant through fifth year
Symptoms return to baseline w/in a few days after discontinuing SNS
Side-effects and Complications
Need to reposition electrode after migration (~20% of patients)

## Slide 6: Percutaneous Posterior Tibial Nerve Stimulation
Percutaneous Posterior Tibial Nerve Stimulation
Technique
Weekly treatment for 10-12 weeks for 20-30 min
Needle inserted 5 cm cephalad (towards the head) from the medial malleolus and just posterior to the margin of the tibia
Also known as Sp-6 point in acupuncture
Tingling sensation felt during stimulation
Evidence
McGuire et al: used acupuncture points in TENS and obtained good symptomatic results
Chang: report results w/ needle technique, showing statistically significant changes in max cystometric capacity and max flow rate
Commercialized as PercSANS
Clinical success rates of 67-81% in ICS (International Continence Society) and EAU (European Association of Urology) congresses of 1999 and 2000
Klingler et al: bladder capacity increased significantly; bladder instability eliminated in 9/13 patients
Long Term Results
Stoller: 81% clinical success rate in 90 patients after mean follow-up of 5.1 years
Patients treated continuously
Reason to start development of minimally invasive peripheral implant device
Side Effects
None reported

## Slide 7: Magnetic Stimulation
Magnetic Stimulation
Electric current (e.g. through a coil) induces magnetic field and changing magnetic field induces an electric field
Can be used to stimulate sacral roots or pudendal nerves noninvasively
Advantage over electrical stimulation is that intensity at level of nerves can be high
Technique
Muscle response of toes used to position coil
Stimulation for 2-5s
Yamanishi: developed chair with coil in seat
>15min of 60s on/30s off 2x/week for 5 weeks
Evidence
Craggs: magnetic stimulation of S3 acutely suppresses provoked contractions in idiopathic and neurogenic patients
Stimulation also abolished sensation of urgency
Yamanishi: inhibition of detrusor activity greater w/ magnetic stimulation compared w/ anogenital electrical stimulation
Long-term Effectiveness
No data on patients w/ pure urge incontinence
Sand et al: 11/16 women w/ mixed incontinence had >50% improvement in number of incontinence episodes/day at 2 weeks after therapy
Side-effects
No serious discomfort

## Slide 8: Intravesical Transurethral Electrostimulation
Intravesical Transurethral Electrostimulation
Based on direct activation of receptors in the bladder to allow patients to recognize urge
Not neuromodulation but closely resembles most neuromodulation techniques
Technique
Catheter w/ stimulation electrode inserted transurethrally into bladder
Treatment 60-90 min 5x/week for 3 weeks
Evidence
First introduced aimed at improving bladder sensation and emptying in patients w/ neurogenic bladder (lack of bladder control due to a brain, spinal cord, or nerve condition), especially children
Suitable candidates are patients in whom at least some neural pathways b/t bladder and cerebral centers are preserved
Application to overactive bladder is relatively new
Hope that patients learn to recognize involuntary contracts and inhibit them by squeezing pelvic floor
Risi et al: advised against intravesical electrostimulation in idiopathic (unknown pathogenesis or apparently spontaneous origin) cases